## Slide 1: CE 3500
Transportation Engineering
Shockwave examples
February 9, 2011

## Slide 2
IN-CLASS EVALUATION

## Slide 3
Pace of the class:
OK – 16.5
Fast – 4.5

## Slide 4
Most unclear topic so far:
Generating an OD matrix – 7
Overall 4-step model process – 3

## Slide 5
Most helpful things:
In-class examples
Posting slides
Reviewing previous classes

## Slide 6
Things which I can do better:
More boardwork
More assignments (*)
Slow down on in-class examples
Too many slides to print

## Slide 7
FOUR-STEP MODEL
AND OD MATRIX
REVIEW

## Slide 8
Back to the four-step model:
What I give you
What you do with it
Results from earlier step

## Slide 9
Trip generation:
Linear regression
Survey results
Attraction equations
Zone data
Calculate productions
Calculate zone attractions

## Slide 10
Trip distribution:
Friction factors
Create OD matrix
Update adjustment factors
Zone productions
Zone attractions
Repeat until rows and columns add up correctly.
Calculate trips starting
and ending in each zone

## Slide 11
Mode choice:
Utility functions
Create OD matrices for bus and car
OD matrix
Calculate proportions by bus and car
Zone data

## Slide 12
Route choice:
Network data
Roadway link volumes and travel times
Vehicle OD matrix
Run route choice program

## Slide 13
Unraveling the mystery of OD matrices
Zone productions
Zone attractions
Calculate trips starting
and ending in each zone
AM Peak: Trips starting in a zone equal work productions; trips ending in a zone equal work attractions.

## Slide 14
Unraveling the mystery of OD matrices
Zone productions
Zone attractions
Calculate trips starting
and ending in each zone
Offpeak: Trips starting and ending in a zone equal sum of shopping productions and attractions

## Slide 15
Unraveling the mystery of OD matrices
Zone productions
Zone attractions
Calculate trips starting
and ending in each zone
PM Peak: Trips starting in a zone equal work attractions; trips ending in a zone equal work productions.

## Slide 16
Friction factors
Create OD matrix
Update adjustment factors
Calculate trips starting
and ending in each zone
Deciphering this formula:
i indicates a row; j indicates a column

## Slide 17
OD matrix value in row i, column j
Column j adjustment factor
Trips starting in row i
Trips ending in column j
Row i and column j of friction factor table
Sum over all columns

## Slide 18
OD matrix value in row i, column j
Column j adjustment factor
Trips starting in row i
Trips ending in column j
Row i and column j of friction factor table
Sum over all columns

## Slide 19
BOARD EXAMPLE

## Slide 20
REVIEW

## Slide 21
Today we focus on the three traffic stream characteristics: speed, flow, and density.
Traffic stream
Space-mean speed (u)
Flow (q)
Density (k)

## Slide 22
More generally, we always have:
q = uk
This is the “fundamental relationship” between speed, flow, and density.
Think units: [veh/hr] = [mi/hr][veh/mi]

## Slide 23
Density (k)
Flow (q)
Speed (u)
Flow (q)

## Slide 24
Density (k)
Flow (q)
How can we get speed from flow-density diagram?

## Slide 25
We can identify “regions” of constant density on this diagram
t
x
I
II
III
IV

## Slide 26
The boundaries between these regions form shockwaves (each red line)
t
x
I
II
III
IV

## Slide 27
These two flows should be the same (no vehicles are appearing or disappearing), so...
A
B
uAB

## Slide 28
ANOTHER SHOCKWAVE EXAMPLE

## Slide 29
Given:
Roadway with free flow speed 60 mi/hr and capacity 1800 veh/hr
Initial speeds are 45 mph
Slow vehicle (20 mph) turns onto roadway at 1 PM, turns off 1
mile later

## Slide 30
Given:
Roadway with free flow speed 60 mi/hr and capacity 1800 veh/hr
Initial speeds are 45 mph
Slow vehicle (20 mph) turns onto roadway, turns off 1 mile later
Find:
All regions and shockwaves; time at which the last vehicle has to slow down to 20 mph