## Slide 1: CE 3500
Transportation Engineering
Trip Generation
January 14, 2011

## Slide 2
ANNOUNCEMENTS

## Slide 3
No class Monday – disregard syllabus
Notes have been posted to website
Would there be interest in moving classroom to engineering building?

## Slide 4
REVIEW

## Slide 5
What do we need to do planning?
Zone structure
Network representation
Data source(s)

## Slide 6
Example: Chicago regional network (1790 zones)

## Slide 7
Chicago regional network has ~12,000 nodes and ~39,000 links

## Slide 8
Trip generation: What are the total number of trips people make to and from each zone?
Trip distribution: What are the specific origins and destinations for this total number of trips?
Mode choice: How many people will choose to drive, walk, ride bicycles, use transit, etc.?
Route choice: What are the specific routes people will use for their trips?

## Slide 9
Trip generation: How many people arrive at UW every morning?
Trip distribution: How many people are coming to UW from each zone?
Mode choice: How many people will drive, walk, use the shuttle, or ride bicycles?
Route choice: What roads will people choose? (This gives information on congestion!)
Example:

## Slide 10
Trip generation: How many people arrive at UW every morning?
Trip distribution: How many people are coming to UW from each zone?
Mode choice: How many people will drive, walk, use the shuttle, or ride bicycles?
Route choice: What roads will people choose? (This gives information on congestion!)

## Slide 11
TRIP GENERATION

## Slide 12
Question #1: How many trips are made by people living in each zone?
Zone
?

## Slide 13
Question #2: How many trips are coming to each zone?
Zone
?

## Slide 14
Usually, we divide trips by purpose (work, shopping, recreation, etc.)
Zone
Why?
Work?
Shop?
Work?
Shop?

## Slide 15
Using travel surveys, we can estimate how many trips a household will make.
3 household members
1 child
2 vehicles owned
Annual income $45,000
1.5 work trips
0.8 shopping trips
(per day)
Trip
generation

## Slide 16
We can then scale this up to the entire zone (since we assume a homogeneous population)
6 households with an average of:
3 household members
1 child
2 vehicles owned
Annual income $45,000
6 x 1.5 = 9 work trips
6 x 0.8 = 4.8 shop trips
(per day)

## Slide 17
Linear regression is used to relate number of trips made to household characteristics

## Slide 18
Linear regression is used to relate number of trips made to household characteristics
Independent variable: Number of trips
Dependent variable(s): Household characteristics

## Slide 19
The line is not exact: no household behaves exactly like the model predicts. But on average it is reasonable.
Independent variable: Number of trips
Dependent variable(s): Household characteristics

## Slide 20
Example linear regression equation.
Work productions (# of work trips)
Dependent variable(s): Household characteristics
Regression coefficients

## Slide 21
Example linear regression equation.
Income
# Vehicles
# Household members
# Workers

## Slide 22
Example linear regression equation.
Income
# Vehicles
# Household members
# Workers
Say income is $50,000, household owns 3 vehicles, contains 5 members (2 are employed)

## Slide 23
Example linear regression equation.
Income
# Vehicles
# Household members
# Workers
Substituting these values in the equation gives 1.6 work trips per day.

## Slide 24
Here’s another equation:
Ps = 0.3 + 0.5(# members) + 0.2(# children) + 0.1 (# cars)
How many trips would a household make with 3 cars, 4 members, and 2 children?

## Slide 25
Here’s another equation:
Ps = 0.3 + 0.5(# members) + 0.2(# children) + 0.1 (# cars)
0.3 + 0.5 x 4 + 0.2 x 2 + 0.1 x 3 = 3.0
How would this number change if they buy one more car?

## Slide 26
Here’s another equation:
Ps = 0.3 + 0.5(# members) + 0.2(# children) + 0.1 (# cars)
0.3 + 0.5 x 4 + 0.2 x 2 + 0.1 x 4 = 3.1
What if they have another child?

## Slide 27
Here’s another equation:
Ps = 0.3 + 0.5(# members) + 0.2(# children) + 0.1 (# cars)
0.3 + 0.5 x 5 + 0.2 x 3 + 0.1 x 4 = 3.8
(Adding a child increases both # members and
# children. Be careful! A change in a household may affect more than one characteristic.)

## Slide 28
This is the approach used for productions (how many trips do households make?)
A similar approach is used for attractions (how many trips will be coming to a particular place?)
Production
Attraction

## Slide 29
Different factors are used, for instance:
Work attractions
(# of people coming to work here)
Household income in this zone
Office space in this zone

## Slide 30
Example from notes:
1. Perform linear regression with survey results (lab next Thursday)

## Slide 31
Example from notes:
2. Substitute zone data (from census)

## Slide 32
Example from notes:
4. Do same with attractions
Production
Attraction

## Slide 33
Example from notes:
5. Scale them so they match
(Each trip consists of one production and one attraction: they have to add up to the same)

## Slide 34
Example from notes:
5. Scale them so they match
Adjust attractions by multiplying them by the right factor so they match productions.