## Slide 1: CE 3500
Transportation Engineering
Mode Choice
January 21, 2011

## Slide 2
ANNOUNCEMENTS

## Slide 3
No class until next Friday
Classroom will change to EN 3070 starting then

## Slide 4
REVIEW

## Slide 5
Trip generation: What are the total number of trips people make to and from each zone?
Trip distribution: What are the specific origins and destinations for this total number of trips?
Mode choice: How many people will choose to drive, walk, ride bicycles, use transit, etc.?
Route choice: What are the specific routes people will use for their trips?

## Slide 6
So, we have more than one OD matrix.
AM PEAK
PM PEAK
OFFPEAK
(everything else)

## Slide 7
Assumptions in this class:
Each work trip produces one journey from the home zone to the work zone during the AM peak, and one journey from work to home during the PM peak
AM Peak
PM Peak

## Slide 8
Assumptions in this class:
Each shopping trip produces one journey from the home zone to the shopping zone during the off-peak, and one journey from shopping to home during the off-peak
Off-peak
Off-peak

## Slide 10
Example:
From the formula
Target we’re trying to get:

## Slide 11
Example:
Previous adjustment factors
New factors:
1
1
1
1
12/13
16/19
48/68
116/92

## Slide 12
Example:
New table
New factors:
12/13
16/19
48/68
116/92
12/13
16/19
(48/68) x (48/50)
(116/92) x (116/115)

## Slide 13
Example:
New table
12/13
16/19
(48/68) x (48/50)
(116/92) x (116/115)

## Slide 14
MODE CHOICE

## Slide 15
There are literally dozens of potential “modes” of travel:
Passenger vehicle
  Drive alone
  Carpool
Taxi
Walk
Bicycle
Public transit
  Bus
  Subway
  Light rail
  Streetcar
  Commuter rail

## Slide 16
There are literally dozens of potential “modes” of travel:
Airplane, helicopter, ferry, gondola, rickshaw, covered wagon, horse, etc. etc. etc.

## Slide 17
To keep things simple, let’s just assume two modes:
  DRIVE PERSONAL VEHICLE
  BUS
  vs.

## Slide 18
To keep things simple, let’s just assume two modes:
  vs.

## Slide 19
What factors would affect this decision for you? Why might someone drive, or why might someone ride the bus?
Location (how close to a bus stop)
Convenience
Cost
Travel time
Parking
Health
Hard constraint
Privacy
Control

## Slide 20
The fundamental idea is that people choose the option with higher “utility” for them.
Utility is a general economic term for “how happy you are with something” taking everything into account.
Fun to drive, get there fast
Don’t have to find parking or worry about damage to car

## Slide 21
Different people and different trip purposes will lead to different utility.
(Road trip)

## Slide 22
(The same framework can be applied to any other choice people make.)

## Slide 23
(The same framework can be applied to any other choice people make.)
Great taste
Less filling

## Slide 24
So, if we can estimate the utility each option provides to people, we can predict what choice they will make.
8,000 people will drive
3,000 people will take bus

## Slide 25
We can define a utility function

## Slide 26
We can define a utility function
Utility of mode m
Properties of mode m and calibrated coefficients
Unobserved factors

## Slide 27
We usually focus on the observed utility
Utility of mode m
Properties of mode m and calibrated coefficients
and deal with the unobserved part later.

## Slide 28
For instance
Income
Travel time
Cost

## Slide 29
Now we can relate these to the census data, and our knowledge of the transportation system.
We need to generate total numbers of people driving or taking the bus. It’s easier to think in proportions Pcar and Pbus.

## Slide 30
A few ground rules:

## Slide 31
A few ground rules:
Pcar is increasing in Vcar
Pbus is increasing in Vbus

## Slide 32
A few ground rules:
Pcar is increasing in Vcar
Pbus is increasing in Vbus
(because of unobserved part... at least some people will choose each option)

## Slide 33
Perhaps the simplest function satisfying these rules is

## Slide 34
Perhaps the simplest function satisfying these rules is
(typo in notes)

## Slide 35
This is the logistic curve:
Proportion choosing car
Vcar - Vbus
0
0.5
1
0

## Slide 36
Check:
?

## Slide 37
Check:
?
Pcar is increasing in Vcar
Pbus is increasing in Vbus

## Slide 38
Check:
?

## Slide 39
Continuing the example, here is the AM peak OD matrix:

## Slide 40
With zone-to-zone travel times and costs by mode, we can use the equation to get mode split.
Travel time (min)

## Slide 41
With zone-to-zone travel times and costs by mode, we can use the equation to get mode split.
Cost ($)

## Slide 42
We can then calculate the observed utility for each mode.
Census data

## Slide 43
We can then calculate the observed utility for each mode.

## Slide 44
Finally, we apply the logistic equation to get mode split.

## Slide 45
Finally, we apply the logistic equation to get mode split.

## Slide 46
If we multiply by the total number of trips going between each zone (dij), we get the total number of trips by mode: